## Slide 1: The Raw Data – Sequencing Traces
Quality drops along the length of the trace.
Base calls added by either ABI or Phred processing software.
Phred also adds confidence values for each base, providing a probability of correct base-calling.

## Slide 2: Typical Base-calling Errors
Base-calling software is not entirely accurate.
Therefore when looking for mutations we need to examine the raw trace data too.
Added base
Incorrect base
Missing base

## Slide 3: Mutations observed in trace data.
Heterozygous – note base call is T and not Y (T/C)
Heterozygous deletion

## Slide 4: Trace Subtraction
Patient
Reference
Difference

## Slide 5: TraceDiff
Aligns traces along X axis.
No Y scaling performed.
Computes difference.
Detect locations where there is a peak both above and below the zero baseline. Peaks in one direction only imply change in the signal strength of one dye without a corresponding change to a different dye. This is typically a “context effect”.
Mutations

## Slide 6: HetScan
Finds superimposed (heterozygous) peaks.
Used in conjunction with TraceDiff to determine the type of mutation.
May also find additional mutations (where the difference trace was too noisy for TraceDiff to trust).
Run on both patient and reference traces to remove false positives caused by trace “compressions”.
Both TraceDiff and HetScan work well on all of our test data and the methods are now being tested by external groups.
For accurate results it is important to sequence both strands.

## Slide 7: Reference traces
Trace peak heights depend on the previous base-calls. Hence we must sequence the reference trace on both strands.
Trace peak shapes depend on the position within the trace, with many broader peaks towards the end. So the reference traces should be sequenced using the same primers as the patient data.
Depending on reproducability of sequencing runs, it may be advisable to reserve two lanes on each plate for repeating the reference trace sequencing.

## Slide 8: Pregap4
Automates processing steps from ABI trace files to aligned database of sequences with annotated mutations.
“Modules” to perform are selected. Example shown here is to specify the reference traces and sequence.

## Slide 9: Gap4 – Contig Editor
Gap4 is the primary tool for sequence navigation and editing.
The above is a screenshot of the “Contig Editor” showing the aligned sequences along with a reference sequence.

## Slide 10: Gap4 – Contig Editor
The “Highlight Disagreements” mode only displays base calls which disagree with the reference sequence.

## Slide 11: Gap4 – Contig Editor
The colours on the first line indicate an EMBL feature.
The red and orange bases are “tags” produced by the automatic mutation detection steps in Pregap4.
Moving the mouse cursor over a tag gives summary information at the bottom of the window.

## Slide 12: Gap4 – Trace Display
Both strands of patient automatically compared against both strands of reference trace to provide rapid visualisation and checking of results.

## Slide 13: Positive and Negative Controls
The reference traces used so for have been negative controls – they represent a wild-type.
We may also specify positive controls, such as trace containing a known disease causing mutation.
The negative control sequences are marked with F and R in the editor. Positive control sequences are marked with f and r.

## Slide 14
Patient traces
Negative control
Positive control

## Slide 15: Reference Sequence
Load an EMBL sequence with features. CDS features used to determine exon locations.
FT CDS 120..5711
FT /codon_start=1
FT /db_xref=”SWISS-PROT:P38398”
FT /gene=”BRCA1”
FT /product=”breast and ovarian cancer
susceptibility”
FT /protein_id=”AAA73985.1”
Used to define a standard numbering for all mutations, regardless of missing base call or alignment issues.
Gene named and amino acid translation shown underneath contig editor consensus sequence.

## Slide 16: Reference Sequence

## Slide 17: Report Mutations
Uses the reference sequence CDS features to determine location and effect of each tagged mutation.
Produces a textual summary of results:
001321_11aF 33885T>Y (silent F) (strand – only)
001321_11aF 34407G>K (expressed E>[ED]) (strand – only)
001321_11cF 35512T>Y (silent L) (double stranded)
001321_11cF 35813C>Y (expressed P>[PL]) (double stranded)
001321_11dF 36314A>R (expressed E>[EG]) (double stranded)
001321_11eF 36749A>R (expressed K>[KR]) (double stranded)
001321_11eF 37313T>K (noncoding) (strand – only)
001321_11eF 36749A>G (expressed K>R) (double stranded)
Name, position, DNA change, amino acid change, strands observed.

## Slide 18: Template Display
Pictorial overview of sequence assembly, showing locations of SNPs.
Reference
sequence
Patient
sequences

## Slide 19
Exon 11 of BRCA1, covered using multiple primers (shown in yellow).
One single reference sequence. A pair of reference traces per set of sequences (i.e. per primer pair).

## Slide 20: Acknowledgements
Rodger Staden
Mark Jordan Staden Package development
Kathryn Beal
Graham Taylor
Andy Wallace Software testing and suggestions
Will Wang
Bonfield, J.K., Rada, C. and Staden, R. Automated detection of point mutations using flourescent sequence trace subtraction. Nucleic Acids Research 26, 3404-3409 (1998)